## Slide 1
Sergey Klimenko
University of Florida
Detection of Gravitational Waves from Core-Collapse Supernovae:
Challenges and Limitations
Cassiopeia A
SN in MW 350 y ago

## Slide 2
SN messengers
  Intense n emission in the first second(s), energy ~ 1051 -1053 erg
  Possible GW emission with energy 1044 - 1048 erg, depending on the model
  This is followed by the Shock Breakout when SN becomes optically visible at cosmological distances by telescopes.
  GW and n are key to SN science
Detection
SN1987A (LMC 53kpc)
Kamiokande (3t) - 11 n
now: SuperK (50t)
2027- HyperK (250t)
also IceCube and JUNO
Expected signal from
MW SN >10000 n
Detectable out to
<1 Mpc with HyperK
few kpc
with HyperK
GW Detection
now: LIGO
2028-: LIGO
upgrades
2035 Cosmic Explorer
Einstein Telescope
Detection
range is
mode/search dependent
Ko Nakamura et.al 2016
1 pc ~ 3 ly
J. Beacom’s talk
Notes: GW detectors are complex and GW search algorithms are mysterious

## Slide 3
Prospects of GW detection from nearby SN
O4 run
  Test a fraction of Galactic models
  Test ALL models for Beetlgeuise
O5 run
  Expect x2 better energy limits
  Start to test bar models
  Test a good fraction of Galactic SN models
3G detectors
  Expect x100 better energy limits due to strain sensitivity
  Can’t miss Galactic SN
  Fair chance of detection out to LMC for optimistic models
for the existing detector and data analysis methodology
BNS
BBH
Szczepanczyk 2024
enthusiastic
realistic
optimistic
Notes: 2

## Slide 4: Detector Response FxH
Noise scaled network antenna patterns
  in general time-frequency dependent
  calculated for each data sample i characterized by noise PSD estimator S[i]
Dominant polarization wave frame:
x
x
NULL (K-2)
network plane
Klimenko et al, 2005
 network data sample
network event 
GW -
noise -
data -
n
Notes: 2

## Slide 5
CE-ET
HL
HL
CE-ET
Network Sensitivity
Acceptance: - sensitivity wrt omnidirectional detectors
Alignment: - fraction of SNR in the hx polarization wrt h+
The CE-ET network may improve GW energy limits by a factor of ~100 due to strain sensitivity and increase the number of detectable events due to the network configuration.
Notes: 1

## Slide 6: GW polarizations
The unique polarization pattern may be distorted by
  noise - results in the pattern dispersion
  network – results in the pattern bias
random
elliptical
linear
circular
y
y
Signal polarization is defined by its pattern
  is 90o phase-shifted network response
  no correlation with other source parameters
NULL space
y
Klimenko et al, 2016
Notes: 2

## Slide 7
Example: elliptical wave patterns
For A~0 network can not distinguish the polarization state of the incoming wave
Capturing GW polarizations
HL
  Full alignment coverage is required for the reconstruction of gravitational wave polarizations.
  It is a gamble to detect a linearly polarized CCSN signal.
Notes: 1

## Slide 8
Detector noise
CQC, v33, n13, 2016
https://cosmicexplorer.org/sensitivity.html
Strain
sensitivity
  Glitches – need more than one detector for confident detection
NULL
glitch
fundamental
noises
glitch
Notes: 2

## Slide 9: Signal Identification
NULL
x=x+n
x
xt
true response
template response
Matched filter
NULL
x=x+n
xp
x
true response
Model-agnostic search
Detection statistics is a projection with xt closest to x (b match), excluding all x where xt = 0
Can recover signals with
noise n
noise n
First, localize excess power with a time-frequency transform
Then, find detection statistics as the best projection of x on the plane
(maximum likelihood solution)
Notes: 2

## Slide 10: Time-frequency analysis
Describe data as a superposition of atomic waveforms (wavelets) with “minimal” TF spread to capture the TF varying spectrum – a large variety of wavelets available
Gabor atoms, 1946  Short Time (windowed) Fourier Transform (STFT)
Organize wavelets in bases, frames, or libraries – a set of wavelets populating the TF plane in a grid with a time/frequency step Dt / Dw.
Gabor wavelets
uncertainty principle
w(t)-window
= w(t)sin(wt)
f = w(t)cos(wt)
w(
=w(
S.Klimenko, July 25, 2025, Warsaw
stsw=0.5 for Gaussian window
st,sw - intrinsic wavelet resolution
Dt,Dw – TF map resolution
classical wavelet
WDM transform

## Slide 11: Time-Frequency Distribution
T=0.064 s
T=0.016 s
T=0.256 s
T=1 s
BBH
chirp
SG
linear chirp
sin(wt)
No optimal localization of power for a single wavelet set (single Gabor window)
General question: How to find the optimal distribution of the time-varying spectrum?
Short Time Fourier Transform:

## Slide 12: Wavescan Transform
New TF transform to address temporal and spectral leakage
  use several (6-8) STFTs with windows of different durations and the same sampling lattice (wavelet stacks)
  selecting optimal resolution by using the overlap Oij between wavelets
  resolution of wavescan wavelets varies over the TF spectrogram
  efficiently remove spectral and temporal leakage
  recover both narrowband and broadband signals
Max Power
12
BBH
SG
linear chirp
sin(wt)
wavescan
(Klimenko, 2022)

## Slide 13: GW150914 and GW170817
L Q-scan
H wavescan
H Q-scan
H Q-scan
L Q-scan
L wavescan
Q-scan
Phys. Rev. Lett. 119, 161101 (2017)
Phys. Rev. Lett. 116, 061102 (2016)

## Slide 14
Search Algorithm
  Coherent WaveBurst: Identify correlated events in two (or more) detectors
  Combine the detector’s data into -excess-power TF map (cWB2G) -cross-power TF map (cWBXP) by accounting for ToF between the detectors
  Identify transient events by selecting excess-power and cross-power pixels above the noise fluctuations
  Use no assumptions on signal waveform: can search for un-modeled & unexpected sources
  used to “for detection of new GW species”, including the first GW detection, GW150914, and the first IMBH event, GW190521
Klimenko 2005, 2008, 2016, 2022
+
=
Time-delayed wavelet amplitudes
wk(i,tk) need to be calculated for
each TF pixel and sky location
(~200000 sky locations)

## Slide 15: Identification of transient events
Identification of weak transient events in quasi-stationary noise starts with the selection of time-delayed () pixels by using the excess/cross power statistics
excess-power cross-power
  Si – power spectral density for detector i
universal pixel statistics
  transform Gamma half-normal
  k – Gamma shape parameter
  - mean of distribution
  - median of distribution
Select pixels above
the threshold
)

## Slide 16: Initial cluster analysis
After the selection of cross-power (black) pixels, contiguous pixel groups are clustered – those are initial clusters. At this stage, the cluster rate is dominated by Gaussian noise.
Both a GW signal and glitches can be highly fragmented – split into two or more initial clusters. At this stage, the event defragmentation is not possible due to a high cluster rate
Identify and remove Gaussian clusters by their size n and by the cluster statistics

## Slide 17: Initial Cluster Selection
For separation of clusters due to quasi-stationary detector noise from GW signals and glitches, the estimator of cluster coherent SNR is used
Where is the wavescan oversampling factor and is the black pixel threshold. For Gaussian noise the statistic follows the exponential distribution (red line).
The initial cluster selection based on reduces the rates by a factor of 1000.
  makes the event defragmentation possible
red
cluster
threshold
clusters selection with
cluster selection with

## Slide 18: Event defragmentation
CCSN signals
  large TF volume – requires low threshold on pixel amplitudes () and cluster SNR ()
  could be highly fragmented – requires de-fragmentation to collect the signal’s power
Initial defragmentation
Final defragmentation
CCSN simulated signal
C15-3D: SNR=29
collected cross-power

## Slide 19: Reconstruction
cWB with WDM and excess-power: collected SNR 11.5, IFAR~1 y
cWB with wavescan and cross-power: collected SNR 12.9, IFAR>1000 y
XP L1
2G L1
The impact of sky localization on CCSN detection confidence is
  moderate for an optical trigger due to poor timing localization of the core bounce
  significant for a neutrino trigger, narrowing the search interval down to a few seconds
It is better to have both triggers
GW190513
C15-3D simulation at 3.3 kpc

## Slide 20: Factors limiting CCSN detection
For CCSN with a large TF volume (~500), the ratio of recovered/injected SNR (rSNR/iSNR) drops significantly for weaker signals
Main limitations
  pixel selection above Gaussian noise by the pixel cross-power statistic
  cluster selection for fragmented events
iSNR=159
rSNR=139
range=0.5 kpc
iSNR=81
rSNR=62
range=1 kpc
iSNR=40
rSNR=27
range=5 kpc
iSNR=24
rSNR=9.3
range=3.3 kpc
Red: small TF volume
Black: large TF volume
O4 noise
C15-3D

## Slide 21: Enhancing CCSN detection
iSNR=24
rSNR=25
range=3.3 kpc
iSNR=24
rSNR=9.3
range=3.3 kpc
CWB cross-power
-315 M pixels per detector map
-6 Tb of data manipulated
O4 noise
CWB cross-power
-315 M pixels per detector map
-6 Tb of data manipulated
CWB cross-correlation
~100 Tb of data manipulated
~ 10 times slower
Can dig deeper into the detector noise with the cross-correlation integrated over a local group of n pixels
CWB excess-power
-70 M pixels per detector map
-0.3 Tb of data manipulated
Increases the complexity of the CWB algorithm

## Slide 22: Pattern recognition
605 606 607 608 609 610. 611
range=3.3 kpc
range=5.0 kpc
range=2.0 kpc
glitch
705 706 707 708 709 710. 711
random noise
Identification of robust signal patterns can be used for reduction of false alarms due to glitches
  similar to the identification of the chirp patterns in cWB BBH searches
Low SNR signal patterns still can be informative, particularly in concurrence with n signals.

## Slide 23: Summary
Expect detections of CCSN signals like D15-3D out to
  ~3 kpc for the rest of the O4 run
  ~5 kpc (preliminary) with the cWB cross-correlation version
Preparation for O5 run
  Deploy a CCSN search targeting realistic signals (input from modelers).
  Run a low-latency CCSN search complementing a n trigger alerts for telescopes.
Future GW detectors at 10 times better strain sensitivity and 1.5 times better sky coverage
  Detection and robust parameter estimation out to 30-50 kpc for D15
  Detection of optimistic models out to 1 Mpc

## Slide 24
SN rates
K. Gill et al, 2023
SN2023ixf
468 166 events per century out to 20 Mpc
1-2 events per century in MW
Galactic SN Cassiopeia A – 350 years ago
Closest extragalactic SN(53 kpc) SN1987A – 36 years ago
The closest SN 2023ixf on LIGO watch: May 19, 2023, 6.7 Mpc
Potential range of n detectors
Notes: Potential LIGO sources:

## Slide 25: Detector response to a GW signal
Direction to the source q,j, and polarization angle Y define the relative orientation of the detector and wave frames.
Rotation of the wave frame Rz(2Y) induces transformations both for F and h, but x is INVARIANT
In the analysis, we have the freedom to select any Y we like.
detector
frame
x
y
z
q,j
Wave frame
h+,hx
x
y
z
Rz(2y)
Antenna patterns
Sampled GW signal
Sampled detector response
Notes: 2

## Slide 26
Factors affecting CCSN detection
Detectors
  Fundamental detector noise (strain sensitivity)
  Non-stationary detector noise (glitches)
  Detector Network configuration
    Confident CCSN detection may not be possible with only one GW detector
Search algorithms
  Exclude data inconsistent with fundamental detector noise.
    Matched filters – identify statistically significant matches across the template bank for each detector
    Burst searches – time-frequency analysis to identify significant excess power, cross-power, or cross-correlation in the detector network
  Event reconstruction – use the maximum likelihood method to extract signal waveforms (parameters)
    Matched filters – best matching template
    Burst searches – superposition of atomic waveforms of limited duration (wavelets)
  Signal identification
    Matched filters – suppress glitches by requiring coincidence of templates across the network, and by the c2 statistics of the residual noise
    Burst searches – use ML statistics (including c2) to find events coherent across the detector network.
Notes: Potential LIGO sources: binary SBH are outside of the LIGO band, binary BH may exist, but never observed before, few binary pulsars (NS) observed in our Galaxy – primary LIGO source

## Slide 27: Signal reconstruction
Likelihood ratio (global fit to the data)
Matched filter for bursts
  Noise model: usually multivariate Gaussian noise
  signal model (detector response)
  find best solution for W=(h+,hx) at maximum of L
    For un-modeled bursts, do variation of L over h+,hx amplitudes
    Use network and signal constraints
Find the signal sky location and waveforms
S-noise covariance matrix
Flanagan, Hughes, PRD 57 4577 (1998)
Klimenko et al, PRD 72, 122002 (2005)
Klimenko et al, CQG 25, 114029, (2008)
Notes: 2